## Slide 1: Asset Management Level II
Jarrett Talley
Capacity Development Supervisor
VDH – Office of Drinking Water
Division of Training, Capacity Development and Outreach
Collaborating across Virginia to Improve the Technical,
Managerial and Financial Capacity of Waterworks
Notes: Brief speaker introduction = My length of time with VDH, previous role as inspector
Feel free to put questions and comments in the chat box, and I will try to address them at the end of each section.
If we don’t get to all of the questions, or you wish to have additional information, my email address is at the end of the presentation.

## Slide 2: Class Overview
Brief recap of Asset Management Concepts
  State of Your Assets
  Assigning Criticality
  Level of Service Goals
Life Cycle Cost Strategies
Funding
Staffing
Notes: We will start with a review of basic asset management concepts, including asset state and assigning criticality. Afterwards we will discuss various levels of service,
And what it takes to achieve service goals set by a utility.
Following the 15 minute break, we will discuss life cycle cost strategies, funding, and staffing. Throughout the presentation there will be numerous resources options available,
Such as templates for Asset Management Plans, links to external sources, charts, etc. If you want me to send you anything in particular, just drop your email address into the chat
box along with what a quick description of what you are looking for.

## Slide 3: What is Asset Management?
A system for monitoring and maintaining things of value (assets) to achieve a desired level of service at the best appropriate cost.
Notes: So we all are using the same definition of asset management, here is a compact way of stating what AM is:
The key terms here are “desired level of service” and “best approximate cost.” Most of the time, what is desired by
The stakeholders Is not cheapest option. An AMP is a tool to you can use to find a common ground between the two.

## Slide 4
Every waterworks
manages its assets:
Proactively
Passively
Reactively
Which one are you?
Group Discussion
Notes: The previous slide said that AM is “monitoring and maintaining” assets. That’s pretty much the same as “managing”.
In everyday life, we are either reactive, proactive, or passive, depending upon the situation.
A reactive water system waits for something to happen and then responds accordingly.
For example 1) Proactive Water System A performs routine maintenance and has a spare pump in the maintenance department.
2) Passive Water System B would simply ignore any pump issues until it completely dies and they have no choice but to get a new one.
3) Reactive Water System C installed a new booster pump in 2005. Since that time, the Have not purchased a backup, have done no preventative maintenance,
and if there is a problem with the pump they do the bare minimum to get it working again.
POLL Question: How would you best describe the current management of your water system? A) Proactive B) Passive C) Reactive D) Combination E) Not Sure

## Slide 5
2. WHICH ASSETS ARE CRITICAL TO SUSTAINED PERFORMANCE?
Notes: 1. WHAT IS THE CURRENT STATE OF YOUR ASSETS? Asset Inventory, Organize, Prioritize Into Asset Hierarchy
2. WHAT IS YOUR REQUIRED SUSTAINABLE LEVEL OF SERVICE? Establish LOS, Policies & Performance Measures
3. WHICH ASSETS ARE CRITICAL TO SUSTAINED PERFORMANCE? Determine Asset Criticality, Conduct Asset Risk Assessments
4. WHAT ARE YOUR MINIMUM LIFE CYCLE COST STRATEGIES? O&M Procedures, Replacement / Repair / Rehabilitation Schedules
5. WHAT IS YOUR BEST LONG-TERM FUNDING STRATEGY? Long-term Funding Plan, Communication Plan, Policy Statements

## Slide 7: 1. What is the Current State of Your Assets?

## Slide 8: Defining Assets
https://www.scwa.com/water-quality/water-education/your-drinking-water/
Notes: This is a diagram created by the Suffolk County Water Authority in New York. Magothy Raritan and Lloyd refer to the Names of Aquifers with the Suffolk County Water Authority.
As we all know, delivering water to customers is far more complex than the average layman realizes.
The assets involved in the process include equipment, buildings, land, people, information, all of the components needed to deliver safe drinking water. After the meter is the customers responsibility.
Large, expensive, long-lived and often buried.

## Slide 9: Where to start?
Notes: Does this slide look confusing to you? Often times when someone is starting to work on an AMP, this is how they feel.
It feels overwhelming to try a find a starting point for so daunting a task.

## Slide 10: Where to Start: Overview
1. Get Approval and/or Build Consensus
2. Identify Your Most Critical Assets
3. Begin Building the Inventory
Important!
Notes: Get approval, but the process is time consuming and therefore costs money.
Start at the top and work your way down. What is the number one thing you can’t do without?
If more than one item, what is the most expensive? Hardest to find?
Just start writing things down. Pen and paper. During the second half of the presentation, we will be interviewing an operator who had to
Make these decisions, and who offers some very good advice on creating an asset inventory.

## Slide 11: Evaluate Assets & Condition
Inventory
As-built plans, specs, maps
Condition of assets
Useful life of assets
Notes: Develop an asset inventory, being as thorough as possible. 2) Locate and include detailed as-builts and system maps. Bear in mind that ODW may have copies on file in
the designated field office if you cannot locate any. 3) Evaluate the condition of each asset utilizing a rating system. 4) A useful life assessment is not the same thing as remaining life.
ASK FOR QUESTIONS.
Now we are going to look at these a little more in detailed.

## Slide 12: VDH Asset Inventory Spreadsheets
http://www.vdh.virginia.gov/drinking-water/office-of-drinking-water/asset-management/
Notes: Condition and Criticality are related to the previous chart. Spots for pumps, distribution, fixed assets, etc. Best condition is a 1, worst condition is a 4. Least critical is a 1. Highest is a 4.
Model, Year, price, all will help when contacting a manufacturer in case of emergency. Note that the Remaining Life Years Column, and the Total Replacement Cost Column, will
Autocalculate.

## Slide 13
http://southwestefc.unm.edu/amkan/main.php
Notes: Very nice introductory guide to an AMP. Southeast Environmental Finance Center Network developed this while working with the State of Kansas.
Interactive with videos throughout. Includes an Asset Management IQ test, testing you and your utilities knowledge Asset Management.

## Slide 14: 2. Which Assets are Critical to Sustained Performance?
Notes: Sustainable performance means your organization efficiently and effectively provides quality products and services.

## Slide 15: Critical Assets
Which assets can fail?
How will they fail?
What is the likelihood of failure?
What is the consequence of failure?
What will it cost to repair the asset?
Notes: Will often see the term criticality when creating an AMP. These are some of the questions you should ask yourself.
Consequence means what is the result or effect of failure?

## Slide 16: Prioritize Response
Notes: To use this chart, start in the lower left-hand corner (on the low-low). Risk is along the vertical axis, Consequence on the horizontal.
As you go up, the amount of risk gets higher.
Risk means the probability that damage or loss caused by external or internal forces could occur (which may have been avoided through preemptive action). As you go right, consequence increases.
Consequence references the result or effect of if an asset fails. Now let’s pretend that sample points A through D represent various pipes in my imaginary water system I shall call The Shire.

## Slide 17: Practice Prioritizing Response
ANSWER: D
Notes: ORIENT AUDIENCE TO SLIDE
Now let’s do a quick exercise to practice using the chart..
The Shire has numerous issues to contend with. First , is this rusted and busted.
LET THEM ANSWER, THEN EXPLAIN ANSWER.
Answer D, Immediate Work: High risk, high consequence. Pipe has totally failed. Needs immediate replacement. Cannot wait, no matter what the cost.

## Slide 18: Practice Prioritizing Response
ANSWER: B
Notes: This pipe has a pin hole leak. The problem just started. There is plenty of spare piping in stock.
Answer B, Aggressive monitoring: High risk, low consequence. Not a matter of if but when.

## Slide 19: Practice Prioritizing Response
ANSWER: A
Notes: This Pex piping was just installed (brand new). It is inexpensive to keep on hand, and easy to find if you run out.
A – Sample Monitoring. Low risk, low consequence.

## Slide 20: Practice Prioritizing Response
ANSWER: C
Notes: While this is an old water tower in The Shire, there are no known leaks or issues. The tank is visually inspected every year. However, the consequences of tank failure are huge. Cost, water shortage.
Answer C: Aggressive Monitoring. Low Risk but High Consequence.

## Slide 21: 3. What is Your Required, Sustainable Level of Service (LOS)?
Notes: Levels of Service relate to what your customers, regulators, decision-makers and staff expect of your assets.

## Slide 22: Determining Level of Service Goals
Start with a Mission Statement
            The NRV Regional Water Authority’s mission is to provide a reliable source of water and safe drinking water to member water systems that include: The Town of Blacksburg, The Town of Christiansburg, Virginia Polytechnic Institute and State University (Virginia Tech), Areas of Montgomery County served by the Montgomery County PSA
Fairfax Water provides its customers
with reliable and abundant water
of exceptional quality at a reasonable
price.

## Slide 23: Managing Expectations
Notes: It’s a balancing act.

## Slide 24: Benefit of a Defined Level of Service
Focused efforts and resources
  On agreed-upon level of service
  Reduces defining LOS arbitrarily or “on the fly”
Clearly communicate service expectations and choices
  Increased services = increased costs
  Discussion of trade-offs and risks
Notes: You will need to re-evaluate what is most important on a regular basis, for EACH expectation individually and as a whole = the bigger picture.
By focusing efforts and resources, Levels of service that are arbitrarily created (on the fly) will be reduced. Everyone is in agreement, no divisiveness;
Clear communication increases the quality of service provided, but increases costs at the same time. Stakeholders need to understand that improvements often come with a price tag.
Will need to discuss what the trade-offs need to be, and the potential risks involved.
Example: The current response time for a leak in The Shire is 4 hours. The stakeholders have determined this is insufficient, and that a 1 hours response time is deemed more
Appropriate. To do this, 2 new staff members will need to be hired, which is something The Shire cannot afford to do at this time. The compromise will be to hire 1 new staff
Member and deal with a 3 hour response time.

## Slide 25: Level of Service Starts with a Conversation
Staff Customers Governing Boards
Other Interested Parties
Notes: While every aspect of the water system is important, you need to select a starting point for prioritization.
Because so many people have a lot to say about LOS, it is important to get them together to discuss what it will mean for the waterworks.
Not only can you get alternate perspectives, you can also educate those external folks.
It’s easier in person to explain the increased cost of responding to a customer complaint within 2 hours versus 6 hours to everyone
At the same times vs each interested party individually.

## Slide 26: Begin with what you know
Review the existing LOS
Notes: Question: Is this a reasonable level of service? If keeping him safe means having to wait 2 hours, then that would be logical decision.
Disparity between the customer wants and what makes sense for the water utility definitely exists.
Utility mission statement, established core principles or goals, baseline measurements of performance
  How do you know if you are accomplishing your objectives?
  What is the demand for my services by my stakeholders?
  What do regulators require?
  What is my actual performance?

## Slide 27: LOS Agreement
Bounded by a Minimum and Maximum (M&M)
Must follow the 3 A’s
  Appropriate
  Acceptable
  Affordable
Notes: Minimum must be set to meet all regulatory requirements. Maximum must be set below the performance capacity of the assets.
Appropriate to systems parameters. Acceptable to stakeholders. Affordable to customers.

## Slide 28: Ideas of Things to Include
Contaminant detection parameters
Water Loss
Length of water outages
Notes: Regulatory parameters will be cost that is then passed on to the customers.
If LOS is to have an extremely low level of contaminants, even lower than State and Fed requirements/PMCLs, then more cost will be involved.
Water loss – calibrate meters, read regularly, monitor fire flow, monitor tanks, to get to 0% vs 12%. IS 0% REASONABLE? CAN ANYBODY ACTUALLY GET TO THAT POINT?
WHEN YOU SET YOUR LOS GOALS, THEY HAVE TO MEET THE REASONABILITY TEST. GO WITH SURVIVABLE AND REASONABLE options, perhaps just a few percent versus 0%. OTHERWISE
YOU COULD SPEND MILLIONS.
Repair records are key to respond to outages, rent equipment, etc. Discover average is 15 hours, which customers say is unacceptable. They want to change to 10. Will need contracts,
Purchase own equipment, pay over time to staff, increased communication with internal and external partners.

## Slide 29: Ideas of Things to Include
Quantity of planned vs. unplanned service interruptions
Percentage of non-revenue water
System flow / pressure parameters
Notes: Number of pipe breaks per mile. Length of time from report to repair.

## Slide 30: Level of Service- What’s the deliverable?
A formalized LOS Agreement

## Slide 31: What it May Look Like
Notes: Specific
Well defined goals are achievable goals.
Is it clear to those with a basic knowledge of the utility? BELOW 20 PSI REQUIRES A BOIL WATER NOTICE.
Measurable
Know if the goal is obtainable and how far away completion is
Know when it has been achieved
Attainable
Capable of being reached
Realistic
Within the availability of resources, knowledge, and time
Time-based
Enough time to achieve the goal
Not too much time, which can affect utility performance

## Slide 32: 4. What are Your Minimum Life Cycle Cost Strategies?
Notes: Life Cycle costing is an important economic analysis used in the selection of alternatives that impact both pending and future costs.
It compares initial investment options, and identifies least cost alternatives over a period of time.

## Slide 33: Life Cycle Costs
https://swefc.unm.edu/iamf/life-cycle-costing/

## Slide 34: Which of these can you control:
purchase price
installation cost
operating costs
maintenance and upgrade costs
remaining value at the end of its useful life
disposal costs
Notes: The purchase price is the price an you pay for your investment, and the price becomes the investor's cost basis for the AMP.
Installation Costs means all costs actually incurred and paid for work performed for the Installation of the asset, as evidenced by invoices, receipts, etc.
Operating costs are the expenses which relate to the operation of the water system, or the operation of a component or piece of equipment at facility. Operating costs are the cost of resources used by an organization just to maintain existence.
Total maintenance cost includes total costed maintenance man hours, parts and any other costs associated with the maintenance effort (preventive and corrective). Upgrading is the process of replacing a product with a newer version of the same type of product.
Remaining value is the estimated value of a fixed asset at the end of its lease term or useful life. Just because you spent $5,000 for a 3hp well pump five years ago doesn’t mean that is what it’s worth. If the manufacturer estimated a life span of approximately 10 years, that means only 5 years of operation potentially remain for the pump. Therefore, you could start with a base remaining value of $2,500. Then take into account how much the pump has ran. If it ran 24/7, the remaining value will drop.
The term cost of disposal is used to describe the incremental expense directly attributed to the disposal of an asset. Cost of disposal is oftentimes a future liability that flows as an expense to the income statement as it is incurred.

## Slide 35: Life Cycle Costs
Plan / Design
Demolish / Dispose
Bid / Construct
Operate / Maintain
Repair / Rehabilitate
Decommission / Replace
Notes: Life cycle costing is a cyclical process which requires identifying options and strategies for your assets, From the Plan/Design Phase all the way through the Demolish/Dispose Phase.
1) Plan/Design Phase, you need to examine the effectiveness of your existing Operating and Maintenance protocols, or procedures.
2) Bid/Construct – Has the original estimated cost of your asset changed? Keep in mind that construction costs can change over 20% within a fiscal year.
3) Operate/Maintain – Review existing O&M costs and capital budgets. Develop an operational improvement plan, and prepare standard procedures for O&M of the asset.
4) Repair/Rehabilitate - Establish basic replacement / repair / rehabilitation guideline. Developing cost / benefit analysis procedures
5) Decommission/Replace - also known as asset retirement, this is the cost incurred by a company when a fixed asset is used up. Decommissioning is the future dismantlement and removal of production equipment and facilities.
6) Demolish/Dispose - Disposal Cost consists of the expenses associated with disposal at the end of an assets useful life. Typically costs could include: Collection/storage/disposal of chemicals, disassembly, safety precautions, transportation to and from the disposal site.

## Slide 36
Adapted from: Gibson and Hamilton (1994) Analysis of pre-project planning effort and success variables for capital facility projects. Construction Industry Institute Source Document 105.
https://swefc.unm.edu/iamf/life-cycle-costing-life-cycle-phases-planning/

## Slide 37
Life Cycle Costs
Without proactive asset management
Excellent
Good
Fair
Poor
Very Poor
Failed
Time
DO NOTHING / OBSERVE
MAINTAIN
REHAB / REBUILD
REPLACE
Notes: This slide emphasizes four phases of life cycle costing in relation to quality and time if you do nothing in terms of asset management.
An asset in good shape typically requires no work, just occasional observation. Once the asset is in fair condition, you will probably find yourself investing some time into maintaining it
In order to keep things running smoothly. A very poor condition asset, such as an old booster pump, will probably have to be rebuilt. The rebuild will only last for so long. Eventually it will fail
And the asset will have to be placed.

## Slide 38
Life Cycle Costs
Excellent
Good
Fair
Poor
Very Poor
Failed
Time
40% drop in quality
First 75% of Useful Life
40% drop in quality
Next 12% of Useful Life
$1.00 spent
for
renewal
here…
will cost
$1.25-$1.50
here …
and
$2.00
here!
Begin planning
here!
Credit: Bill Jarocki, Former Director, Boise State EFC
Notes: When the asset is in excellent shape and newly installed, asset quality is at it’s highest. As quality deteriorates over time, the cost to replace the asset increases. The best time to start investing is now!
Spend $1 to renew a booster pump early on makes the most sense financially. Once the asset reaches a fair condition, you will experience a 40% drop in quality
And the First 75% of useful life has passed. As this time, you will need to spend $1.25-$1.50 to renew the asset. Waiting until the asset is in very poor condition, or fails, will result in a $2.00 investment.
Basically your costs double.
Pay me now or pay me later…. One way or another we have to pay.

## Slide 39
Life Cycle Costs
Excellent
Good
Fair
Poor
Very Poor
Failed
Time
Operational costs
Notes: The chart is just like the last slide, with asset quality and time being accounted for. As you can see, there is a sharp increase over time in operational costs.
An increase in operating expenses means less profit for the water utility.
Often operating expenses receive the most scrutiny, as these types of costs may be less fixed than non-operating expenses and capital expenditures.

## Slide 40
Life Cycle Costs
Excellent
Good
Fair
Poor
Very Poor
Failed
Time
Proactive Management
Normal Deterioration Curve
Minimum Service Standard
$1.00
Notes: Here is the same slide again, but this time showing what happens if you invest money proactively into the management of your asset. A new bar is shown here called Minimum Service Standard.
This line represents meeting the minimum costs of maintaining an asset over the cost of its life in order to provide the minimum level of service to your customer (inspections, upkeep, etc).
Following the Normal Deterioration Curve down to the point of the asset being in Good condition, we see the Proactive Management pink dotted line intersect and then go upwards.
This jump reflects a $1.00 investment into the asset in order to pump it back up to Excellent condition. Over time, investing a $1 a couple of times will continue to keep the asset in tip-top shape.
By doing this, you will stay about the Minimum Service Standard over a greater length of time.

## Slide 41
Life Cycle Costs
Excellent
Good
Fair
Poor
Very Poor
Failed
Time
Rehab
Normal Deterioration Curve
Minimum Service Standard
$1.25-$1.50
Notes: By waiting until the asset is in Poor condition, you have dipped below the Minimum Service Standard. You will need to invest 25-50% more money just to bring the asset up to a Good level.
You have also reduced the amount of time you will stay above the Minimum Service level.

## Slide 42: Operations vs Maintenance
Standard Operating Procedures (SOPs)
Preventive Maintenance Procedures (PMPs)
Notes: Standard Operating Procedures (SOPs) = Step-by-step instructions compiled to help workers carry out complex routine operations. SOPs aim to achieve efficiency, quality output and uniformity of performance, while reducing miscommunication and failure to comply with industry regulations. Example: Collecting bacti water samples from a distribution point.
Preventative Maintenance Procedures (PMPs) = Unlike corrective or reactive maintenance (which involves generating a work order request in response to an existing failure), preventive maintenance helps prevent failures from happening in the first place. Examples: Valve Exercising Program and a Unidirectional Flushing Program.
POLL Question: How many of you have written Standard Operating Procedures in place that are actively being practiced? Yes or No

## Slide 43: Operations vs Maintenance
Corrective Maintenance Procedures (CMPs)
Emergency Operating Procedures (EOPs)
Notes: Corrective Maintenance Procedures (CMPs) = The chief disadvantage of this maintenance procedure is the inherent amount of uncertainty associated with it. Extremely reactive in nature, CM is capable of shutting down an entire operation because of a single failure. Steps to a CMP may include: Once the failure has been detected, it must be confirmed. If the failure is not confirmed, the item generally is returned to service. This no-fault-found problem leads to a considerable waste of time at significant cost. It also entails carrying an unnecessarily large inventory all the time. If the failure is confirmed, the item is prepared for maintenance and the failure report is completed. Localization and isolation of a failed part is the natural next step in corrective maintenance. The failed part is then removed for disposal or repair. If disposed of, a new part is installed in its place. The item may be reassembled, realigned, and adjusted after repair. It is checked before being put back to use.
Emergency Operating Procedures (EOPs) = A bit different than CMP in that you can’t plan for the maintenance, it must happen immediately, such as the pump shown in this slide.

## Slide 44: 5. What is Your Best Long- Term Funding Strategy?
Notes: Long-term planning includes the overall goals of the company set four or five years into the future, usually based upon reaching medium-term targets.
Planning in this way helps you complete short-term tasks while keeping longer-term goals in mind.
LTFS is important because it allows you to budget a portion of your revenues or profits over a period of several years. This allows you to properly fund new initiatives without weakening your current operations or financial position.

## Slide 45: Long-Term Funding Strategy
Answer the following questions Yes or No:
Does your utility have enough money to maintain its assets to meet its required level of service?
Is your utility’s rate structure sustainable for the system’s long-term needs?
Is it affordable for the community?
Are you/the board/owners/partners making sound financial decisions?
Notes: Sound financial decisions and developing an effective long-term funding strategy are critical to the implementation of an asset management program.
Knowing the full economic costs and revenues generated by your water system will enable you to determine your system’s financial forecast. Your system’s financial forecast can then help you
decide what changes need to be made to your system’s long-term funding strategy.
Some strategies to consider include: • Revising rate structure. • Funding a dedicated reserve from current revenues and
• Financing asset rehabilitation, repair, and replacement through borrowing or other financial assistance.

## Slide 46: Rate Structure
https://www.wunc.org/post/nc-water-systems-need-26b-says-deq
Notes: Even though this slide is for the state of North Carolina, it closely mimics Virginia’s infrastructure needs and funding sources.
While some funding is available, realize that the customer will be footing the largest portion of the bill.
Grants and external funding sources are limited and very competitive. As you can see, even with all of the external funding organizations combined,
Only 7% of costs are covered. 93% of needs are either payed by the utility or deferred.

## Slide 47: Utility Pricing Strategies
Base Fees
Volumetric Charges
Structured Tiers
Location / Customer Differentials
Up-Front or “Buy-In” Fees
Availability Fees
Notes: Utility pricing strategy is often used to help determine rates. It is a model or method used to establish the best price for the product/service. It helps a system choose prices to maximize profits and shareholder value while considering consumer and market demand. The strategy may include for example:
Base Fees, which use and structure a minimum usage and dollar amount (example $25.00 for first 2000 gallons of water)
Locational Differentials, such as lower in-rates and higher out-of-town rates
And Customer Differentials: Is the water connection for a residential, commercial, or industrial location? Should the industrial user be charged more? Or less?

## Slide 48: Taking Asset Management to the Next Step…
Asset Management is about knowing you are focusing limited resources on the right projects at the right time.
Notes: The right project and the right timing go hand in hand. The installation of a new water main may be needed, but trying to do the project
During COVID, when revenues are down and staff is minimal, is probably the wrong time to start.

## Slide 49: The Capital Improvement Plan
Planning for specific projects
Long-term capital asset funding
Creation of a Capital Reserve Fund
Notes: Once a good AMP is established, the groundwork for successful service delivery for future generations can be set.
A CIP functions as a planning and funding mechanism for investment in long-term capital assets.
It also establishes a basis and authority for the development of Capital Reserve Funds.
CIP development should be governed by a written policy to be adopted by an elected body, and communicated publicly.

## Slide 50
Capital Investment Plan
Annual Operating Budget
Capital Improvement
Plan
20 – 30 YEARS
10
YEARS
5
YEARS
1
YEAR
PLANNING PERIOD
Repair & Replacement
Schedule
Notes: When you decide to work on a CIP, one of the first questions you may ask is How far out should I plan?
Most small water systems only operate in the current fiscal year with their Annual Budget.
If you are able to plan a CIP, they typically are scheduled out to about 5 years, followed by a 10 year repair/replacement schedule. But what is a repair/replacement plan?
Think about the repair/replacement plan for a refrigerator. When you buy the refrigerator new, you have the option to buy the repair/replacement plan for an additional $20/month.
The plan works similarly for water utilities. Investing money on a regular basis into a plan or fund will help to offset labor costs and out-of-pocked expenses when issues arise with your system.
The last phase of planning is Capital Investment, scheduling 20-30 years out.
A capital investment is a long-term growth strategy. A company plans and implements capital investments in order to ensure its growth in the future. Capital investments generally are made to increase
operational capacity, capture a larger share of the market, and generate more revenue. If possible, start planning now in order to allow for expansion.
Each year is a re-adjustment.

## Slide 51: Minimum CIP Components
Project Description
Year Needed
Cost Estimate
Funding Sources
Resulting Changes in Operations
Impact on LOS
Notes: Here is a general list of what you should include when creating your CIP list.
Include a description of the project along with a brief statement regarding the need for the project.
Concerning the anticipated year of the project, state whether it is absolute or flexible. Some things just cannot wait, while others are no rush.
Estimate project cost along with data illustrating how the costs were determined.
Provide a list of the potential funding sources considered, or available, for the type of project you are creating. ODW? Bank Loan? USDA?
And finally list the changes in overall operations that may occur as a result of the project, and how they may impact your LOS
(including but not limited to operator requirements, additional O&M costs, regulatory changes, etc.)
POLL Question: Do you know which sources are available to get the funding you need? Yes or No
For those who answer No, email for a list.

## Slide 52: CIP Evaluation Criteria
Expected Life of Improvement
Scheduling
Percent of Population Served
Public Support
Notes: The Capital Improvement program is based on an extensive prioritization process. Projects are prioritized based on critical objectives and strategies.
When it comes to drinking water, a project that improves public health and the safety of the community should be rated with the highest priority.
Projects should demonstrate the benefit provided to the community and possible risks from not completing the project. Compliance with state and federal mandates fall under this category.

## Slide 53: A Capital Reserve Fund Is…..
Savings account or other highly liquid asset
Designated for capital expenses
For the expected and unexpected
For designated projects only
Notes: A dedicated funding stream specifically earmarked for capital projects. The fund should only be used for approved and prioritized projects.
This may be a percentage of annual revenue, a lump sum budget line item, or the dedication of interest earnings. The money should be designated for specific projects and/or a structured debt service.
This will requires fiscal discipline, basically protecting reserves from being used for non-utility needs.
For example: A County decides to dissolve the local Service Authority, and merge all assets with the County. At that point, reserves are in danger of being utilized for non-water related items.

## Slide 54: The People in Asset Management
Notes: Now let’s talk about the most important asset in any business – the people.

## Slide 55: The People in Asset Management
Broadening the vision of Asset Management to include Hidden Assets:
Customers
Employees
Knowledge Base (Institutional Knowledge)
Notes: There was a time when employers could expect their staff to "stay put" until retirement. Those days, along with the guaranteed pension and loyalty to employees that came with them, are gone.
Today's employers face higher turnover rates than at any other time in history, especially in the drinking water industry.
Many organizations lack sufficient transfer programs to stem the loss. Plans must be in place to ensure continuity.
What would this type of plan look like? It may include strong employee/employer communications, reviews, work processes, finding alternative ways to get the work done, and adopting technology.

## Slide 56: Role of Employees
Providing Customer Service: The face of the organization
Performing complex procedures
Knowing what works
Deploying resources
Notes: Lots of responsibility is on your shoulders to provide customers a high level of service.
If a management strategy doesn’t work, you will be one of the first people to know. At that point you have to decide how to proceed.
Do you just go with it, or do you try and fix it? Based upon that strategy, you will have to decide which resources are needed to provide customers with clean, safe drinking water.
Managers please remember that without buy-in from your employees, a waterworks will not have an effective asset management model.

## Slide 57: The role of Customers in Asset Management
Does your waterworks have open (two-way)
communications with customers?
Does your waterworks have defined customer LOS
established?
Do you solicit feedback from customers on utility performance?
What do you do with that feedback? How do you measure performance?
Notes: Even though the old adage “The customer is always right” isn’t entirely accurate, we still need to consider the public when working on our AMP.
Two-way open communication, LOS, and KPIs are important considerations to keep in mind.

## Slide 58: Tools to Get You There

## Slide 59
The Waterworks Business Operations Plan
Notes: A WBOP incorporates everything we have discussed in this presentation (AMP, CIP, procedures) into one location. It is a living document, used to effectively organize your waterworks system. While lengthy and often times painful,
It is a process well worth it. Especially if your water system is considering DWSRF funding from ODW (or any organization for that matter) in the near future.
POLL Question 1: How many of you have a WBOP? Yes or No
POLL Question 2: How many of you actually use the WBOP? Yes or No

## Slide 61: Waterworks Business Operations Plan
Part 1: Waterworks Information
Part 2: Staffing
Part 3: Management, Operations & Procedures
Part 4: Planning
Part 5: Financial Information
Part 6: Sustainability Improvements
Part 7: Worksheets & Supporting Documentation
Part 8: Statements for Owner Signature
https://www.vdh.virginia.gov/drinking-water/capacity-development/waterworks-business-operations-plan/

## Slide 62
Notes: The Community Excel spreadsheet we provide is a tool to help you plan for reserves, adjust water rates, etc.
Again, don’t worry about perfection. At the bottom of the spreadsheet, based upon the data you enter, the form predicts
If you are Sustainable or Not Sustainable over time. If you find numerous fields are listed as Not Sustainable, such as
Revenues greater than expenses, this is your chance to experiment with rate increases and see what it will take to improve.

## Slide 63: Resources
VDH Capacity Development Webpages:
AMP
  https://www.vdh.virginia.gov/drinking-water/capacity-development/asset-management/
  WBOP
  https://www.vdh.virginia.gov/drinking-water/capacity-development/waterworks-business-operations-plan/
EPA’s Clean Water and Drinking Water Infrastructure Sustainability Policy:
  http://water.epa.gov/infrastructure/sustain/Clean-Water-and-Drinking-Water-Infrastructure-Sustainability-Policy.cfm

## Slide 64: Need Help?
https://efcnetwork.org/
Notes: If you need help with setting rate structure, the EFCN has tools and staff in place to help. All of their assistance and free and confidential.

## Slide 65
https://swefcamswitchboard.unm.edu/am/
Notes: A paper which aligns asset management strategy with level of service. This 5-page document discusses topics such as establishing levels of service, getting customers involved, and understanding
And balancing costs.

## Slide 66
Geographic Information Systems (GIS)
Identify trends in water main breaks to prioritize pipe replacement and rehabilitation projects.
Analyze soil conditions, surrounding area
Coordinate with other systems
Record and analyze current conditions
Notes: 80-90% of a utility is tied to locational data
  Pipes, valves, meters, etc.
Where crews are working
What facilities need to be repaired/replaced
The digital representation of a water or wastewater utility’s network typically includes pipes, meters, valves, manholes, and other critical facilities referenced to some sort of land base background of streets, parcels, contours, and political boundaries. This as-built picture provides the what, where, and when of the utility’s history. However, the same data are extremely useful in looking forward - especially when integrating the GIS with other data sets and applications.

## Slide 67
Notes: Lots of software options. Lots of different price points.
The GIS Department of the Central Shenandoah Planning District Commission performs spatial analysis, GPS data collection, and map production for regional, local, comprehensive and strategic planning projects for our member jurisdictions and agency planners.
Boardroom Quality Maps, GIS Project Management, GIS Consulting Services, GIS Training & Education, just to name a few. Less expensive than engineering firm, for example, but potential waiting list.

## Slide 68
https://swefcamswitchboard.unm.edu/am/the-five-core-components-of-asset-management/life-cycle-costing/
Notes: This website has a user-friendly set of on-line process and practice guidelines, templates and decision support tools that will:
Simplify AMP development, Provide effective Implementation Guidelines, Drive meaningful improvements in asset management.
The users of this website will be: Asset managers and operators, Appointed and elected officials, Engineering consultants

## Slide 69
https://www.wbdg.org/resources/life-cycle-cost-analysis-lcca
Notes: Life-cycle cost analysis (LCCA) tool is used assessing the total cost of facility ownership. It takes into account all costs of acquiring, owning, and disposing of a business. It is especially useful when there are various project alternatives that fulfill the same requirements, and you need to decide which option to go with. With respect to initial costs and operating costs, comparisons need to be made in order to select the option that maximizes net savings.
For example, LCCA will help determine whether the incorporation of a VFD or conventional pump system is best. You may find that the VFD will increase initial cost, but result in dramatically reduced operating and maintenance costs. LCCA is not useful for budget allocation.
ANY QUESTIONS?

## Slide 70: Contact Info:
Jarrett Talley
Capacity Development Supervisor
VDH - Office of Drinking Water
Jarrett.talley@vdh.virginia.gov
Cell (804) 317-0140