## Slide 1: Treatment Techniques
Virginia Tech Short Course
Jamie Morris
Western Virginia Water Authority
1

## Slide 2: Introduction
Survey what the contaminants are in drinking water,
How they are categorized and regulated
Overview of techniques to remove contaminants

## Slide 3: Agenda/Housekeeping
Definition/Vocabulary
Contaminants
Regulations
Processes and techniques for removal
Treatment alternatives for VOCs and THMs

## Slide 4: Overview
The big picture is you are responsible to produce water that is safe to drink
Your career is in Public Health
To do this you must know what can make water unsafe, and how to operate, control and monitor the product and ultimately report and communicate to your consumers

## Slide 5: Vocabulary- Treatment & Standards
Treatment- take the supply source water and remove those constituents which cause negative health and aesthetic effects
Primary standards- health related contaminants with numerical limits
Secondary standards- aesthetics related, guidelines such as for iron, sodium, manganese, etc.

## Slide 6: High Quality Water
Turbidity less than 0.05 NTU
Particulate matter smaller than 2 um (micron=1/100mm)
Free of microorganisms
Very low in organic carbon
Very low in disinfectant residual
Low Pb/Cu leaching potential
Very low in disinfection by- products
Reliable and available at all times

## Slide 7: What Is Safe?
Reasonable risk
Nothing is risk- free

## Slide 8: Types of Contaminants in General
Chemical-
  natural
  man-made
Microbiological
Disinfection Byproducts

## Slide 9: EPA Regulates Contaminants
18 major drinking water regulations for 91 contaminants from 1976-2006
In 2001, EPA lowered arsenic’s limits
The EPA has also finalized new standards for certain PFAS chemicals (2024)

## Slide 10: EPA Regulations and Contaminants
EPA shall regulate a contaminant if:
The contaminant may have an adverse health effect;
The contaminant is known or likely to occur with a frequency and at levels of public health concern; and
3. (National) regulation presents a meaningful opportunity for health risk reduction

## Slide 11: EPA Contaminants
Inorganic compounds (IOCs) (Ex. Pb)
Volatile organic chemicals (VOCs) (Ex. CHCl3)
Synthetic organic compounds (SOCs) (Ex. Pesticide)
Microbiological contaminants (Ex. E. coli)
Radionuclides (Ex. Radium – 226)
Disinfectants and their by-products (DBP) (Ex. THMs/HAA5s)
PFAS (six compounds)

## Slide 12: The Number of EPA Regulated Contaminants
100
90
80
70
60
50
40
30
20
10
0
1979
1987
1989
1991
1992
1995
1998
2000
2010

## Slide 13: Primary Inorganic Contaminants (IOC) Regulated by EPA
Antimony
Arsenic
Asbestos
Barium
Beryllium
Cadmium
Chromium
Copper
Cyanide
Fluoride
Lead
Mercury
Nitrate
Nitrite
Selenium
Thallium

## Slide 14: VOC & SOC Regulated by EPA
trans-1,2-Dichloroethylene
Hexachlorocyclopentadiene
Xylenes
Acrylamide | Dichloromethane | Lindane
Alachlor | 1,2-Dichloropropane | Methoxycenol
Atrazine | Di(2-ethyhexyl) ylbenzene | Oxamyl
Benzeme | Ddipate | Polychlorinated biphenyls (PCBs)
Benzp(a)pyrene(PAHs) | Di(2-ethylhexyl) phthalate | Pentachlorop
Carbofuran | Dinoseb | Picloram
Carbon Tetrachloride | Dioxin | Simaxine
Chlordane | Diquat | Styrene
Chlorobenzene | Endothall | Tetrachloroethylene
2,4-D | Endrin | Toluene
Dalapon | Epichlorohydrin | Toxaphene
1.2 Dibromo-3-chloropropane | Etthylenebenzene | Silvex
o-Dichlorobenzene | Ethylene dibromide | 1,2,4-Trichlorobenzene
p-Dichlorobenzene | Glyphosate | 1,1,1-Trichloroethane
1,2-Dichloroethane | Heptachlor | 1,1,2-Trichloroethane
1,1-Dichlorethylene | Heptachlor epoxide | Trichloroethylene
cis-1,2-Dichloroethylene | Hexachlorobenzene | Vinyl chloride

## Slide 15: VOCs
Volatile, low solubility in water, man-made solvents (carbon tet, benzene, vinyl chloride)
Total Halogenated Organic Chemicals (TOX) is used to measure with “broad brush”
From lab studies on mice, some are carcinogenic
Extrapolate risk to humans with 70 year exposure to risk of 1 per million
More prevalent contaminant in groundwater
THMs are volatile and treated similarly, but are different category

## Slide 16: Microbiological-Three Agents of Waterborne Disease
Agent | Bacteria | Protozoa | Viruses
Examples | E. coli Salmonella Legionella | Giardia Crypto- sporidium | Hepatitis Polio Norwalk
Size | 1 um | 3-25 um | 20-30 nm
Notes: What is a protozoa? Microscopic unicellular eukaryote. What’s a eukaryote? An organism whose cells contain a nucleus within a membrane.

## Slide 17: Microbes indicated by Total Coliform
Total Coliform Bacteria itself does not cause disease
It is an indicator of source water quality, proper treatment and disinfection and integrity of distribution system
Notes: You might hear the term indicator species. That is referring to total coliforms.

## Slide 18: What is Total Coliform?
Numerous types of gram negative bacteria
Rod shaped
Feeds on lactose
Produce acid and gas within 48 hours @ 35 degrees C
They have the enzyme galactosidase
They are ubiquitous
Notes: Bottom line: They hang out with fecal coliforms. They will show up before the fecal coliforms. So, they can be a warning. Total coliforms can be present without fecal coliforms. Fecal coliforms will never be present without total coliforms being present. E. coli is one species of fecal coliform.

## Slide 19: Why Don’t We Monitor Pathogens Directly?
Pathogen concentrations are very low and can be easily missed
The test methods are difficult to reproduce
The monitoring is not real time, it takes days for results
Expensive
Surrogates or indicators have been effective in past
E. coli and fecal coliform are other more specific tests

## Slide 20: Turbidity Measurements
Turbidity along with total coliform/fecal coliform/E coli is an indicator
Turbidity is not a microorganism but is a measure of the particulate matter in water
Indicates the potential number of organisms present and the effectiveness of treatment and removal of contaminants.
Notes: Turbidity being present is a two-fold problem. It allows a place for coliforms to hide blocking it from the disinfectant. Turbidity eats up chlorine (i.e. is a source of chlorine demand).

## Slide 21: Total Trihalomethanes (TTHM)
Chemical interaction of chlorine with natural organics (TOC) in water
These are a special type of VOC created in the treatment process when chlorine is used to control microbiological contaminants
MCL of 0.08 mg/l locational running annual average (LRAA)
Notes: What’s LRAA? The average of sample analytical results for samples taken at a particular monitoring location during the previous four calendar quarters. You may also hear of OELs. Operational Evaluation Levels. Calculated for both TTHMs and HAA5s at each monitoring location using Stage 2 DBPR compliance monitoring results. OEL is determined by the sum of the two previous quarter’s TTHM or HAA5 result plus twice the current quarter’s TTHM or HAA5 result at that location, divided by four. OEL = (Q1 + Q2 + 2Q3) / 4. This calculation is not to determine compliance, but is a tool to help predict a potential problem.

## Slide 22: Haloacetic Acids (HAA)
Nonvolatile products formed by chlorination of organic materials
Lumped as one regulated contaminant that includes five different types (HAA5)
Generally lower in concentration than TTHM
MCL of 0.06 mg/l locational running annual average (LRAA)

## Slide 23: Secondary Contaminants by EPA are considered guidelines. SMCL’s and not enforced
Aluminum
Chloride
Color
Copper
Corrosivity
Fluoride
Foaming Agents
Iron
Manganese
Odor
pH
Silver
Sulfate
Total Dissolved Solids
Zinc

## Slide 24
1 mg/L =1 ppm = 1,000 ppb
1 ug/L = 1 ppb = 1,000 ppt
1 ng/L = 1 ppt
1 part per million equals 1,000 parts per billion
Notes: When we talk about PFAS compounds we are now talking about parts per trillion. Another way to think about it is, one (1) ppt would be represented by a single drop of water in 18 million gallons of water. That is one drop of water in roughly 20 Olympic sized swimming pools.

## Slide 25
Example of THM sampling in the the distribution system-
highest LRAA = 72.5*
The systemwide average =55**
Date | Maple Avenue | Main Street | Water Street | Lovers Leap | Average
Spring | 30 | 40 | 50 | 60 | 45
Summer | 40 | 50 | 60 | 90 | 80
Fall | 40 | 50 | 50 | 80 | 55
Winter | 30 | 30 | 40 | 60 | 40
LRAA 2023 Va Tech Wa | 35 ter Treatment Short | 45 Course | 50 | 72,5* | 55**

## Slide 26: Emerging Contaminants
MBTE (A fuel additive in gasoline)
Algal and cyanobacterial toxins
Pesticides
NDMA from chloramination
Nitrogenous DBPs from chlorination
Endocrine disrupting compounds (EDC)
Pharmaceuticals
C8 from Teflon (PTFE)
GenX (HFPO-DA)
These two compounds are part of the PFAS group.

## Slide 27: Unregulated Contaminant Monitoring Rule (UCMR)
Five year cycle
Completing UCMR5
Select 30 potential contaminants
Sampled & Tested nationwide survey

## Slide 28: Treatment Techniques
Water treatment facilities are designed based on the raw water quality and the characterization and concentration of contaminants to be
removed

## Slide 29: Treatment Techniques
Hypochlorination Other disinfection Corrosion control
BAC
Coagulation Sedimentation
Aeration
Activated carbon
Iron and manganese removal Ion exchange
Membrane technology Slow sand filtration

## Slide 30: Treatment Technique Alternatives
 | Aeration | Oxidation | Carbon Adsorp- tion | Coagula -tion
SOC | NO | YES | YES | Maybe
VOC | YES | YES | YES | Maybe
THM | YES | Maybe | YES | NO
THM precursor | Maybe | Maybe | YES | YES
Notes: What is a THM precursor? TOC

## Slide 31: Typical Stages of Water Treatment
Pre- treatment
Coagulation Flocculation Sedimentation
Filtration
Disinfection
Post- treatment
Distribution
Compare these 6 stages with
Salem WTP tour this afternoon.
System

## Slide 32: Pretreatment-pH Adjustment or Oxidation
Lime- increases pH
Carbon dioxide- decreases pH
NaOH- increase pH
Acid- decrease pH
Aeration- in ground water strips out CO2,VOCs or oxidizes iron
Oxidants besides air

## Slide 33: Other Pre-treatment Techniques
33
Presedimentation
Bank Filtration
Watershed Control and Algae Control
Covered Storage

## Slide 34: Conventional Treatment Flocculation/Coagulation
Lime
Alum
Ferric/Ferrous salt
Polymer (Cationic/Anionic)

## Slide 35: Bench Scale or Jar Test
Simulate plant conditions and performance
Optimal removal for turbidity and TOC as a precursor for DBPs
Pace chemical dosage according to varying raw water quantity and quality

## Slide 36: Physical Size Separation Techniques
Sedimentation by gravity
Filtration
Reverse osmosis
Ultrafiltration
Membrane filtration
Adsorption

## Slide 37
37
2023 Va Tech Water Treatment Short Course

## Slide 38: Filtration
Condition influent properly (filter aid, softening)
Operate the filter properly in service and when backwashing
Turbidity is the most common measure of effective filtration, 0.3 ntu at least 95%
Spikes are an issue, 1.0 ntu limit
Monitor each individual filter

## Slide 39: Micro Filtration/Ultra Filtration
Membrane cartridge production costs are dramatically reduced
Ability to remove pathogens to 1 um
Requires less space or footprint
Fits relatively easily to upgrade existing treatment

## Slide 40: MF/UF Issues
What to do with the sidestream or waste
Type- encased or submerged
Degree of pretreatment required
Testing for “leaks”
Flux changes over time (surface loading rate)

## Slide 41: Disinfection
Chlorine
UV
Chloramines
Chlorine Dioxide
Ozone

## Slide 42: Techniques for controlling THM
Remove the THM precursors by adsorption in granular or activated carbon (GAC and PAC), improve TOC removal in coagulation/sedimentation process or oxidize out with ozone
Remove the THM after they form aeration, adsorption in granular or powdered activated carbon
Change the type of disinfectant to prevent them from forming such as ozone, chlorine dioxide, chloramines or UV

## Slide 43: Factors Affecting THM formation
Precursor Type- some organics make more THMs.
Contact Time- contact means better disinfection BU T THMs increase
pH – higher pH- lowers THMs
Temperature – higher temperature means higher THMs
Chlorine Residual – lower residual means lower THMs Residual Type – chloramines reduce THMs
Bromide Concentration – higher Bromine means higher THMs
Precursor Concentration – higher precursor means higher THMs

## Slide 44: Aeration Removes THM and VOC
Transfer VOC & THM from liquid phase (water) to gas phase (air)
Diffused compressed air
Mechanical aerators
Packed tower

## Slide 45
Pre- treatment
Coagulation Flocculation Sedimentation
Filtration
Disinfection
Post- treatment
Distribution
Aeration can be used to
remove VOC precursors in
Pretreatment OR
Remove volatile THMs after Disinfection (Post- treatment)
System
Notes: Note: Tank aeration that strips THMs/HAA5s also strips out your disinfection residual.

## Slide 46: VOC & THM removal by air stripping equipment - Waterfall Aeration (Packed Tower)

## Slide 47: Adsorption with Granular or Powdered Activated Carbon
SOC, VOC & THM diffuse into the pore space of the carbon grain
There are different carbon sizes (GAC or PAC)
There are different carbon sources from peanut shells, coconut shells to oak
Contact time is function of application rate or loading and depth of media
Notes: PAC is fed into the treatment process ahead of sedimentation. GAC requires a contactor (pressure vessel or open bed filter) with an underdrain. You will need to backwash GAC. PAC is point of use and is a single use. It has to be fed constantly like a treatment chemical.

## Slide 48: Adsorption- carbon pores adsorb contaminants
Carbon structure showing the small and large adsorbed chemical molecules diffused into the pore space

## Slide 49: Carbon Adsorber Operation in Series

## Slide 50: Post Treatment
Fluoridation
pH adjustment
Pb/Cu corrosion inhibition

## Slide 51: Contaminants after Treatment in the Distribution System
2023 Va Tech Water Treatment Short
Course
Disinfection by-products
Pb/Cu
Nitrification
Cross connections

## Slide 52: Summary
What the contaminants are
How to remove THM and VOC